## Slide 1
a
Study region and spring migration direction field
Onshore wind farm (n = 4,191)
Offshore farm, VPTS radar (n = 29)
Offshore farm, Bauer grid (n = 26)
Weather radar station (n = 6)
Spring migration direction concentration
0.85
0.90
0.95
1.00
Mechanism chain (b → f): array orientation, not siting alone, sets exposure
b
Migration field φ
2,025 cells; mean bearing 52 deg, concentration 0.89
φ ≈ 52°
c
Array orientation θ
Exposure is purely geometric: E ∝ sin²(θ − φ)
φ
θ ∥ φ
low exposure
θ ⊥ φ
high exposure
d
Energy vs ecological optimum
Median misalignment 48 / 40 / 45 deg; bars = IQR
0°
30°
60°
90°
misalignment Δ (°)
e
A small rotation captures most of the gain
Δθ₅₀ = 17° onshore; a ≤20° rotation already captures 55% of the avoidable exposure
Chart: rotation Δθ (°)
| 0 | 3 | 6 | 9 | 12 | 15 | 18 | 21 | 24 | 27 | 30 | 33 | 36 | 39 | 42 | 45
VPTS | 0 | 11.3 | 22.7 | 34 | 44.1 | 53.6 | 63.1 | 71.6 | 78.1 | 75.4 | 82.2 | 82.7 | 87.4 | 84.3 | 76.8 | 75.5
Bauer | 0 | 9.2 | 18.3 | 27.5 | 34.4 | 42.7 | 50.9 | 56.1 | 62.9 | 68.7 | 75.5 | 80.4 | 83.6 | 84.3 | 76.1 | 80.6
Onshore | 0 | 9.2 | 18.3 | 27.1 | 35.5 | 43.1 | 50.5 | 57 | 63 | 68.9 | 73 | 77.1 | 81.1 | 84.2 | 86.4 | 87
≤20°
f
A ≤1% AEP budget buys nearly all of it
At a 1% AEP budget the median exposure cut is 97% onshore, 84% VPTS, 48% Bauer
Chart: AEP budget (%)
| 0.5 | 1 | 2 | 5
Onshore | 80.03 | 96.94 | 99.07 | 99.26
VPTS | 77.25 | 84.24 | 84.24 | 84.46
Bauer | 37.73 | 47.62 | 70.56 | 89.28